Foellinger Theatre

3411 Sherman Blvd. - GPS Address 3191 Sherman Blvd.

Fort Wayne, IN 46808

www.foellingertheatre.org

Stage Specifications

Proscenium opening is 56 feet by 28 feet trimmed to approximately 19 feet with grand teaser (can be removed upon negotiation)

Grid Height is 63 feet from the stage floor

Proscenium Line to back wall 35 feet to most shallow point

Orchestra pit is covered and is stage worthy

Soft goods include 2 full stage travelling black drapes, one Grand drape at proscenium line, one poly-cyc backdrop, and five border curtains overhead

3 Front of House Rigging Points rated at 2,000 lbs. each

2 Front of House Pick Points

No Front of House Sounds Points

Projection Screen

Dalite 19’ x 25’ Fastfold frame permanently hung mid-stage (flies)

Lighting

Dimming and Control

ETC Element console

Strand CD80 2.4 K dimmers hardwired to our electrical battens immediately adjacent to down stage right

ETC 24 2.4K Dimmer pack with Socapex cables

Distribution / Circuiting (see theatre circuit plan)

2 front catwalks

Proscenium arch lighting ladders on each side

Side pipes above the stage left and right off stage areas (do not fly)

5 electrical pipe battens over the stage (counterweighted and will fly)

Fixtures

30 ETC Source 4 19 degree ERS lamped at 750 watts

80 ETC Source 4 par lamped at 750 watts

30 1,000 watt ProCan par lights on 6 light bars

3 pro can 8 light audience blinders

8 ETC Source 4 12 cell Multipars lamped at 750 watts

Various Strand SL 26 and 36 degree fixtures

Follow Spotlights

4 Phoebus Imarc 850 follow spotlights

Hazers

2 DF 50 hazers

Intercom / Headsets

Production Intercom 8 stations Clear com compatible

Loading Dock

Loading dock is immediately adjacent to upstage left

One dock with overhead door

Portable dock plate

Sound

Speakers

18 JBL Professional VRX 932LA1 in three line arrays 6 cabinets per array (hung from catwalk)

Subs

4 JBL SRX 728S Dual 18”

Consoles

FOH

Yamaha M3000 (40 inputs)

Monitor

Yamaha 32x6 analog console

JBL 15” two-way passive floor wedges (6)

DSP

BSS digital signal processor

*Microphones and stands

Theatre is well equipped with multiple units of common microphones

Mulitple stand sizes and configurations

*Audio Department head will advise upon advance

Promoter’s Production Company must provide audio snake to go around seating.  There is no conduit through the house.  Minimum length 250 feet preferred length 300 feet. House will provide ADA cable ramps.

*Power

400 Amp 3 phase down stage right (cam-locks)

200 Amp 3 phase down stage left (cam-locks)

100 Amp 3 phase up stage left

Platforms

13 Stage Right double sided reversible all purpose stage deck

4 Stage Right Z800 24 inch reconfigurable stage supports

7 Stage Right Z800 16 inch reconfigurable stage supports

7 Stage Right Z800 8 inch reconfigurable stage supports

2 Stage Right 8 inch single steps (no railing)

2 Stage Right 16 inch steps (no railing)

4 Stage Right 8 feet long chair stops

Plan View of Foellinger Theatre

Full theatre

http://www.fortwayneparks.org/images/stories/Facilities/foellinger-theaterschematic.pdf

Stage

http://www.fortwayneparks.org/images/stories/Facilities/foellingerstage.pdf

For Additional Information Contact Theatre Manager

tim.byers@cityoffortwayne.org

(260) 427-6018